## Slide 1
Logic Design Project
LCD1602 and DHT-20 Sensor Expansion Shield for STM32 Nucleo Development Board
HO CHI MINH CITY UNIVERSITY OF TECHNOLOGY
FACULTY OF COMPUTER SCIENCE AND ENGINEERING
COUNCIL: COMPUTER ENGINEERING 2
INSTRUCTOR: Ph.D. LÊ TRỌNG NHÂN
01
Cao Minh Quang
2052221
02
Lê Tuấn Hưng
2052508
03
Trần Cao Duy Trường
2052299

## Slide 2
Contents
01
Introduction
02
Devices and Components
03
04
05
System & Program Design
Demonstration Result
Conclusions & Perspectives
01

## Slide 3
A brief overview of the project target
Information about the expansion shield
01
Introduction
02

## Slide 4
Device Drivers
Practice implementing device drivers for different devices.
Hardware Design
Enhance skill in circuit design, soldering components and debugging.
MCU - MPU Course Practical Usage
Apply technical skill in C programming language and defining FSMs.
Hardware Communication Protocol
Understand the working principle of UART & I2C and apply them in the project.
03
Project Target

## Slide 5
LCD 1602 and DHT-20
Expansion Shield
  The DHT20 sensor is used to measure temperature and humidity.
  The LCD displays measured value.
  2 header extension for I2C devices.
04

## Slide 6
I2C Communication Protocol
LCD1602 & PCF8574AT
DHT-20 Sensor
02
Devices &
Components
05

## Slide 7
STM Nucleo Development Board with STM32F103RBT6 MCU
  Core: ARM 32-Bit Cortex-M3 CPU
  Memories: 64 or 128 Kbytes of flash memory and 20Kbytes of SRAM
  Peripherals: DMA, Motor Control PWM, PDR, POR, PVD, PWM, Temp Sensor, WDT
  Speed: 72MHz
06

## Slide 8
Why using LCD1602 with PCF8574
  The PCF8574/74A helps to convert data signal to perform an I2C communication to the LCD.
  Using I2C reduces the connection from 12 to only 4 pins.
  Easier to maintain code flow.
07

## Slide 9
DHT-20 Sensor
  High-performance semiconductor silicon-based.
  I2C Output Signal.
  Capacitive humidity and temperature sensor.
08

## Slide 10
I2C Protocol Working Principle
The main function of STM32 HAL library for I2C:
  HAL_I2C_IsDeviceReady( );
  HAL_I2C_Master_Transmit( );
  HAL_I2C_Master_Receive( );
09

## Slide 11
Advantage of I2C Communication
  Reduce the number of PINs need for connection.
  Multiple-master and multiple-slave flexibility.
  ACK/NACK bit gives confirmation
that each frame is transferred
successfully.
10

## Slide 12
Hardware design with Altium Designer 21
Block diagram for the system
Proposal architecture for the system
Finite state machines
03
System &
Program Design
11

## Slide 13
Schematic
Schematic library provide by Chipfc
Design on Altium Designer
Version 21.6.4
12

## Slide 14
Footprint library and
3D model provide by Chipfc
PCB Layout
13

## Slide 15
Block diagram for the system
14

## Slide 16
Proposal Architecture
15
  A command has the form !'content'#.

## Slide 17
FSM for command parser
  This FSM acts as a signal generator for the operation of the system.
16

## Slide 18
FSM for the whole system
  This FSM will intercept the signal and perform the associated action.
  The software timer is called every 10ms.
  In each call, the counter will be decreased by 1.
  So setTimer(100) is equivalent to 1 second timer.
17

## Slide 19
Present the functionality of the shield
04
Demonstration
Result
18

## Slide 20
05
Conclusions &
Perspectives
19

## Slide 21
Conclusions
I2C Communication Protocol
  Research and implement the shield with I2C devices.
  Understand the properties and behavior of the devices.
LCD 1602 & DHT-20 Sensor
  Propose an architecture and implement the fully operative system.
Expansion shield
20

## Slide 22
  Expanding to IoTs direction with air purifier system.
  Adding more sensors for PM 2.5 dust and harmful gases detection.
  Mobile application to display, notify, supervisor, and control the system.
Perspectives
21

## Slide 23
This is the end of our presentation.
Thank you so much for your attention !
Logic Design Project - Semester 221